## Slide 1: GREC Fuel Types
3 main types:
In-woods
  Agricultural and forestry land management activities including site prep, fire fuels reduction, salvage, land clearing
Urban
  Including curbside yard debris, storm debris, tree service and land clearing debris
Mill residues
  Primary and secondary wood-using mills: sawmills, chip mills, truss and pallet plants

## Slide 2: GREC Typical Fuel Characteristics
Type | Moisture content | Ash content | Btu/dry lb
In-woods | 36 - 42% | < 2% | 8,450
Urban | 25 - 45% | 2% - 10% | 8,200
Mill residues (dry) | 12% | < 1% | 9,100
Mill residues (green) | 45 - 52% | < 1% | 9,100

## Slide 3: GREC Fuel Availability
In-woods
  > 5 million acres of timberland in GREC supply shed, generating > 7 million tons of conventional roundwood products
  Logging residues and other agricultural land management activity generate > 1 million tons of fuel wood
Urban
  > 700,000 tons of urban wood waste generated within an economic haul distance to GREC
Mill residues
  Primary wood-using mills in supply area generate > 2 million tons of residues

## Slide 4: GREC Historic Fuel Sourcing
 | Tons |  |  | 
Year | In-woods | Urban | Mill residue | Total
2014 | 526,085 | 196,074 | 39,346 | 761,505
2015 | 394,738 | 44,536 | 36,134 | 475,408
2016 | 37,299 | 2,071 | 17,540 | 56,910
2017 | 181,819 | 15,904 | 6,837 | 204,560

## Slide 5: GREC Supply Chain Characteristics
> 20 fuel producers of all types
In-woods producers (7): all have chip equipment; most with trucking capacity, others contract trucking
Urban producers (>10): most have grinders; some have trucking
Average haul distance for in-woods fuel typically 50-55 miles; urban often greater (Jacksonville, I-4 corridor)

## Slide 6: GREC Fuel Costs
Delivered fuel costs function of: type/quality, distance, diesel fuel prices, moisture content, dispatch characteristics
Most fuel contracted for on a dry weight basis
Fuel contracts contain adjusters for diesel fuel prices
Urban fuel typically has adjusters for ash content
Costs for all fuel reflect the distance that it is hauled
Unpredictable dispatch conditions increase fuel costs

## Slide 7: Fuel Supply Overview
Summary of fuel sourcing 1/1/17-6/30/17:
Category | As-rec’d. tons | MC | $/as-rec’d. ton | $/dry ton | $/MMBtu | % Furnish
In-woods | 181,819 | 39.7% | $ 28.75 | $ 47.65 | $ 2.82 | 88.9%
Mill residue | 6,837 | 26.1% | $ 28.59 | $ 38.71 | $ 2.13 | 3.3%
Urban | 15,904 | 30.7% | $ 22.40 | $ 32.31 | $ 1.97 | 7.8%
TOTAL | 204,560 | 38.5% | $ 28.25 | $ 45.94 | $ 2.72 | 100%
6

## Slide 8: Fuel Procurement Staffing
4 full time positions: Fuel Procurement Manager, Biomass Forester, Quality Control Technician, Scale Attendant
Development and maintenance of fuel supply chain.
Fuel delivery scheduling and preparation of fuel payments.
Operation of scales and ticketing system; facilitation of truck dump operation.
Fuel quality control oversight including in-house analysis of fuel moisture and ash content.
Oversight of forest-sourced fuel Minimum Sustainability Standards (MSS).
Forest Stewardship Council (FSC) Controlled Wood and Chain of Custody certification maintenance.
7